## Slide 1: Discrete Event Simulation

## Slide 2: Discrete Event Simulation
Imitating the operation of a system over time.
Typical objective- Support decisions related to the use of limited resources.

## Slide 3: Discrete Event Simulation - Outline
To understand how and why we simulate such systems we will cover:
  Analysis options.
  The mechanics of how a simulation is implemented on a computer.
  Modeling views/orientations.
  The steps of a simulation study.
  Analyzing input and output data.
  Simulating randomness.

## Slide 4: Analysis Options
Utilize the simplest fastest methods that provide adequate decision support

## Slide 5: Analysis Options
Resource allocation decisions – It may suffice to examine resource utilizations and WIP.

## Slide 6: Example
A workstation has two machines in parallel that can process jobs at a rate of 15 JPH. Jobs arrive over time at a rate of 25 JPH.

## Slide 7: Analysis Options
Unless a system has very high relative variability, utilizations < 90% will lead to “reasonable” queue sizes.
  Demo

## Slide 8: In-class Exercise
Two types of jobs (A and B) arrive to a single machine for processing. The arrival rate of type A jobs is 5 per hour, and 2.5 per hour for type B jobs. Type A jobs have an average service time of 5 minutes, and type B jobs have an average service time of 11 minutes.
  What is the utilization of the machine?

## Slide 9: Analysis Options
At the next level of detail queuing models may be applied.
  More information than utilization calculations.
  Difficult skill to apply.
  Some G/G/m models were covered in IE 368.

## Slide 10: Discrete Event Simulation - Basics
Fundamental components/terminology.
Simulation mechanics
  Manual execution of a simulation.
Performance measures.

## Slide 11: Terminology
We will simulate stochastic dynamic discrete-event systems.
  Stochastic –
  Dynamic –

## Slide 12: Terminology
Discrete event –
  System state –
  Examples

## Slide 13: Terminology
Entities – Objects that move through the simulated system.
  Examples
    Entities can be combined and split.

## Slide 14: Terminology
Attributes – Parameters, data specific to an entity.
  Examples
  The same concept as objects (entities) and object data (attributes) in Object Oriented Programming

## Slide 15: Terminology
Global variables/parameters – System wide values accessible by all entities and resources.
  Examples
  Resources – Items that are used by entities and found in limited amounts.
  Queues – Spaces where entities wait for resources.

## Slide 16: Terminology
Events – Actions that cause the system state to change.
  Examples

## Slide 17: Mechanics of Simulation
Event calendar and the passage of simulated time.
  Simulations maintain an event calendar that functions like the control center of the simulation.
  The event calendar is a time sorted list of events and the times that they occur.
  When the event at the top of the list occurs, simulated time is advanced and specific logic is initiated.
    This logic changes the state, updates statistics, and schedules additional events.

## Slide 18: Event Calendar
Main
Procedures/
Functions
Computer Program

## Slide 19: Simulation Clock
Simulation time does not advance uniformly unless controlled.
Arena demo
x
x
x
x
x
x

## Slide 20: Manual Simulation
We will execute a manual simulation on paper to understand the fundamentals of simulation mechanics.
You will execute what the computer carries out in a simulation.

## Slide 21: Example System
A “single server queuing system with infinite queue capacity”.
System description
  Customers (jobs) arrive one at a time to be processed by a server who can serve a single customer at a time. If the server is idle when a customer arrives the customer immediately starts service, otherwise the customer waits in an infinite capacity queue and is served in first-in-first-out (FIFO) order.

## Slide 22
…
Queue
Arrivals
Server
For some fixed simulated time:
How many customers are processed?
What’s the average customer queue time?
What’s the average customer system time?
What is the average number in queue?
What is the server utilization?
What are max observed values for
  Queue time?
  Time in system?
  Number in queue?
Example System

## Slide 23: Manual Simulation
Will use pseudo code and a table to implement the simulation.
See handout.

## Slide 24: Manual Simulation Table

## Slide 25: Notation
t = simulation time
tbefore = prior event simulation time.
Q(t) = # in queue at time t
B(t) = 1 if the server is busy, and 0 if the server is idle
P = the number of customers/jobs processed after each event
N = the number of customers/jobs that have passed through the queue
∑WQ = the sum of the queue times observed for customers
WQ* = Max queue time observed
∑TS = the sum of the system times (queue + service) observed for customers
TS* = Max system time observed
∫Q = the area under the Q(t) curve through time t
Q* = Max value for the number in queue observed
∫B = the area under the B(t) curve through time t

## Slide 28
Simulation time
Q(t)
0
Simulation time
B(t)
0
1
0

## Slide 29: “Simulation Performance Measures”
Simulation performance measures
  Tally statistics –”Tally” is an Arena term.

## Slide 30: “Simulation Performance Measures”
Simulation performance measures.
  Counters – Incremented when specific events occur.
    E.g., Completed jobs.
  Time average measures – Arena calls these “Time persistent”

## Slide 31: “Simulation Performance Measures”
Simulation performance measures.
  Maximums and minimums – Changed when specific comparisons indicate.
    E.g., Maximum jobs in queue.

## Slide 32: “Simulation Performance Measures”
The average time a part spends in the system.
  Tally or Time average?
Utilization of a machine.
  Tally or Time average?

## Slide 33: In-class Exercise
Compute the average number in system, and average time in system through T = 14 (assume first-in-first-out).

## Slide 34: In-class Exercise

## Slide 35: Simulation Modeling Views
The manual simulation looked at the system dynamics by examining the events that occur.
  This is called event orientation.
Event orientation

## Slide 36: Simulation Modeling Views
Process orientation – The focus on defining the system dynamics is on entities and how they flow through the system.
Manual simulation.
  Arrive-> Queue -> Machine -> Depart
Arena is process orientated simulation system.
Process orientation tends to be easier when modeling large systems.
Most simulations are implemented in an event driven manner (including Arena).

## Slide 37: Initial Steps in a Simulation Study
Define the objectives of the study.
Write a description of the system.
List assumptions if any.
Write a report introduction.
From the system description identify
  Data collection needs

## Slide 38: Intermediate Steps
Begin model development.
Fit distributions to data for use in the model.
Verify and validate the model.
Experimentation and analysis.

## Slide 39: Final Steps
Report writing.
Presentations.
  Animation if necessary
Other points.
  On going communication throughout the study.
  Observation/face time.